## Slide 1: Microcontrollers and FPGAs
Embedded Systems

## Slide 2: Verilog
Verilog is a Hardware Description Language (HDL).
It is a surprisingly big language, but most of its instructions are useful for simulation only. The number of structures that can actually be put in an FPGA is much smaller.
An HDL is not a programming language, it is a formalism for describing digital logic. As such, it’s vitally important that you understand how every piece of Verilog that you write will actually look when it has been synthesized in to hardware.
If your Verilog isn’t working, try sketching the logic gates and registers yourself. If you can’t make your Verilog look like good hardware, then the synthesizer probably can’t either!
Two primary classes of logic: Combinatorial and Sequential

## Slide 3: Verilog
Combinatorial logic with assign statements

## Slide 4: Verilog
Combinatorial logic with always statements

## Slide 5: Verilog
Rules for combinatorial circuits:
No feedback allowed.
assign or always(*) statements may be used.
  Assigns are more compact and often used for simple wiring tasks like assign reset_n = key[0];
  Always statements are more flexible and lead in to sequential logic
  The signals between the brackets in the always statement is called the sensitivity list. You don’t need to have a ‘*’ for combinatorial logic, you can list each input signal separately, however if you forget to enter a signal then the logic is no longer strictly combinatorial and may not synthesize as you expect.
Wrong!

## Slide 6: Verilog
If statements

## Slide 7: Verilog
If Statements:
Synthesize to two distinct pieces.
  A wire representing the outcome of the test
  A multiplexor that selects the correct input signal given the above wire
Cases should be complete! They don’t strictly have to be, the below code is valid, but the synthesizer will create latches for to cover the unused case. Latches are almost never what you actually want.

## Slide 8: Verilog
If Statements:
Also note that two latches no not equal a correct multiplexor. The synthesizer will probably not be smart enough what you meant with the code below, even if it’s obvious to you
always @(*) begin
if (&InVar1) begin
OutVar1 = InVar1;
end
end
always @(*) begin
if (!(&InVar1)) begin
OutVar1 = ~InVar1;
end
end

## Slide 9: Verilog
Case Statements:
If statements are special case statements.
Like if statements, case statements synthesize to two parts:
  A wire (generally a bus of wires) representing all possible selections of the case statement
  A multiplexor that selects the correct input given the above wire
Like if statements, they should be complete to avoid the generation of latches

## Slide 10: Verilog
Sequential logic
The ‘D’ flip-flop

## Slide 11: Verilog
Sequential logic:
Use non-blocking assignments, i.e <=
Always block sensitivity list should be edge-triggered
  always @(posedge clk)
All signals inside the block must be registered to the clock edge. If your logic is working intermittently, try registering your wires before use
In sequential blocks, if and case statements need not be complete. Unmatched cases effectively synthesize to OutVar <= OutVar

## Slide 12: Verilog
Important point: What is the ‘System Clock’?
When talking about sequential logic, we’ve been talking about a system clock. This is often simply a net routed from a pin in the top level file
If this clock rate is not right for you, what do you do?
reg [1:0] my_clock;
always @(posedge clk) begin
my_clock <= my_clock + 1;
end
always @(posedge my_clock[1]) begin
…
end
Wrong!

## Slide 13: Verilog
Why? Internally my_clock[1] is a logic net, not a clock net (gclk in Altera-speak). This won’t matter for slow-speed designs, but as speed increases the time it takes for a logic signal to propagate through the chip begins to matter.
This is our first example of having to think about things in the time domain but it won’t be our last!
The correct way to do this is to have the external clock in the sensitivity list but use my_clock[1] in the always body to drive a state machine or otherwise determine what to actually do.

## Slide 14: Clocks
The exception is when you can use dedicated hardware on the chip to modify the clock and route it back on to a gclk.
The clock infrastructure of the Cyclone IV part on our DE2 boards is pictured here.
If you need a clock that can’t be generated easily by the tricks on the previous slide, you can use a Phase Locked Loop (PLL)

## Slide 15: Clocks
A PLL is instantiated like any other Verilog sub-module but the synthesizer recognizes that it’s special and builds the logic out of a PLL hardware block instead of generic gates.
PLLs and a host of other pieces of logic can be created using the Altera MegaCore Plugin Wizard. The generated code to turn a 50MHz clock in to 100MHz is shown to the right, obviously not the sort of thing you want to write by hand.
altpll altpll_component (
.inclk (sub_wire3),
.clk (sub_wire0),
.activeclock (),
.areset (1'b0),
.clkbad (),
.clkena ({6{1'b1}}),
.clkloss (),
.clkswitch (1'b0),
.configupdate (1'b0),
.enable0 (),
.enable1 (),
.extclk (),
.extclkena ({4{1'b1}}),
.fbin (1'b1),
.fbmimicbidir (),
.fbout (),
.fref (),
.icdrclk (),
.locked (),
.pfdena (1'b1),
.phasecounterselect ({4{1'b1}}),
.phasedone (),
.phasestep (1'b1),
.phaseupdown (1'b1),
.pllena (1'b1),
.scanaclr (1'b0),
.scanclk (1'b0),
.scanclkena (1'b1),
.scandata (1'b0),
.scandataout (),
.scandone (),
.scanread (1'b0),
.scanwrite (1'b0),
.sclkout0 (),
.sclkout1 (),
.vcooverrange (),
.vcounderrange ());
defparam
altpll_component.bandwidth_type = "AUTO",
altpll_component.clk0_divide_by = 1,
altpll_component.clk0_duty_cycle = 50,
altpll_component.clk0_multiply_by = 2,
altpll_component.clk0_phase_shift = "0",
altpll_component.compensate_clock = "CLK0",
altpll_component.inclk0_input_frequency = 37037,
altpll_component.intended_device_family = "Cyclone IV E",
altpll_component.lpm_type = "altpll",
altpll_component.operation_mode = "NORMAL",
altpll_component.pll_type = "AUTO",
altpll_component.port_activeclock = "PORT_UNUSED",
altpll_component.port_areset = "PORT_UNUSED",
altpll_component.port_clkbad0 = "PORT_UNUSED",
altpll_component.port_clkbad1 = "PORT_UNUSED",
altpll_component.port_clkloss = "PORT_UNUSED",
altpll_component.port_clkswitch = "PORT_UNUSED",
altpll_component.port_configupdate = "PORT_UNUSED",
altpll_component.port_fbin = "PORT_UNUSED",
altpll_component.port_inclk0 = "PORT_USED",
altpll_component.port_inclk1 = "PORT_UNUSED",
altpll_component.port_locked = "PORT_UNUSED",
altpll_component.port_pfdena = "PORT_UNUSED",
altpll_component.port_phasecounterselect = "PORT_UNUSED",
altpll_component.port_phasedone = "PORT_UNUSED",
altpll_component.port_phasestep = "PORT_UNUSED",
altpll_component.port_phaseupdown = "PORT_UNUSED",
altpll_component.port_pllena = "PORT_UNUSED",
altpll_component.port_scanaclr = "PORT_UNUSED",
altpll_component.port_scanclk = "PORT_UNUSED",
altpll_component.port_scanclkena = "PORT_UNUSED",
altpll_component.port_scandata = "PORT_UNUSED",
altpll_component.port_scandataout = "PORT_UNUSED",
altpll_component.port_scandone = "PORT_UNUSED",
altpll_component.port_scanread = "PORT_UNUSED",
altpll_component.port_scanwrite = "PORT_UNUSED",
altpll_component.port_clk0 = "PORT_USED",
altpll_component.port_clk1 = "PORT_UNUSED",
altpll_component.port_clk2 = "PORT_UNUSED",
altpll_component.port_clk3 = "PORT_UNUSED",
altpll_component.port_clk4 = "PORT_UNUSED",
altpll_component.port_clk5 = "PORT_UNUSED",
altpll_component.port_clkena0 = "PORT_UNUSED",
altpll_component.port_clkena1 = "PORT_UNUSED",
altpll_component.port_clkena2 = "PORT_UNUSED",
altpll_component.port_clkena3 = "PORT_UNUSED",
altpll_component.port_clkena4 = "PORT_UNUSED",
altpll_component.port_clkena5 = "PORT_UNUSED",
altpll_component.port_extclk0 = "PORT_UNUSED",
altpll_component.port_extclk1 = "PORT_UNUSED",
altpll_component.port_extclk2 = "PORT_UNUSED",
altpll_component.port_extclk3 = "PORT_UNUSED",
altpll_component.width_clock = 5;

## Slide 16: Clocks
Aside: A fully-functional FM radio transmitter using a PLL in 7 lines:
pll clockgen(clk, clk2);
always @(negedge clk)
begin
ctr <= ctr + 1;
pwm <= wav_dat < ctr[7:0] ? 0 : 1;
end
assign out = pwm ? clk : clk2;
Cheated a bit, not shown is the bit that loads wav_dat with the current waveform point, nor all the definitions.
Get a 100MHz carrier using a Wizard-generated PLL
Generate a PWM signal with duty cycle proportional to the sound data
The output is just the carrier clock modulated by the PWM signal

## Slide 17: Clocks
Aside: A fully-functional FM radio transmitter using a PLL in 7 lines:
pll clockgen(clk, clk2);
always @(negedge clk)
begin
ctr <= ctr + 1;
pwm <= wav_dat < ctr[7:0] ? 0 : 1;
end
assign out = pwm ? clk : clk2;
Cheated a bit, not shown is the bit that loads wav_dat with the current waveform point, nor all the definitions.
Get a 100MHz carrier using a Wizard-generated PLL
Generate a PWM signal with duty cycle proportional to the sound data
The output is just the carrier clock modulated by the PWM signal
Project idea!

## Slide 18: Finite State Machines (FSM)

## Slide 19: FSM

## Slide 20: FSM
Let x(t) - input, s(t) - state, z(t) - output
Moore machine:
  s(t+1) = F(s(t), x(t)) −state equation
  z(t) = G(s(t)) −output equation
Mealy machine:
  s(t+1) = F(s(t), x(t)) −state equation
  z(t) = G(s(t), x(t)) −output equation
ENGN3213 only uses Synchronous State Machines;

## Slide 21: FSM

## Slide 22: FSM in Verilog http://www.altera.com/support/examples/verilog/ver_statem.html

## Slide 23: FSM – Design Steps
1. Determine the inputs / outputs. Determine the states and give them
mnemonic names
2. Draw up a state diagram and a next state table.
3. Render the inputs, outputs and states in binary format (VERILOG
parameter).
4. Draw an excitation table
5. Draw an Output table
6. Use K-maps to obtain produce minimal next state and output
combinational logic.
7. Use the standard VERILOG formulation to simulate your design and check
for correct operation. Revise as appropriate.
8. Check for potential practical problems (e.g. non-ideal effects).

## Slide 24: Microprocessors
MU0
A realistic but simple processor which is capable of executing one instruction every two clock cycles.
We won’t be looking at this in labs, but the data path and control flows will be used in illustrating many of the more advanced topics in microprocessors over the coming lectures

## Slide 25: Microprocessors
Timing is important to understand. The processing of a single instruction is split in to two parts, one per clock cycle: Fetch and Execute.
Thus each instruction takes two clock cycles to complete.
Actually there are four states with two occurring on the falling edges. This is valid as MU0 is simple and runs slowly. When we get to more complex systems, we’ll note that these extra states are made explicit

## Slide 26: Microprocessors
During the Fetch cycle, the Program Counter is wired in to the memory address, and the instruction at that location is loaded in to the Instruction Register.

## Slide 27: Microprocessors
The Execute phase is centred around the Arithmetic Logic Unit (ALU). It takes two operands, one of which is always a register (either the Accumulator or the Program Counter depending on the operation). The other is either a memory location whose address is coded in to the instruction, or some portion of the instruction itself.

## Slide 28: Microprocessors
This basic structure is very similar across all CPUs. Here we see the CPU portion of the Atmel ATMega8 microcontroller.
Program Counter, Instruction Register, ALU, Memory busses all pretty much the same.
Differences: MU0 has one working register, ACC, Mega8 has 32 (6 of which can be paired in to 3 special registers, XYZ, of twice the size). Different memory architecture, MU0 has a single memory to hold instructions and data, the AVR has two blocks labeled Program Flash and SRAM respectively.

## Slide 29: Microprocessors
The Nios2 core we will be using in labs is more complex again, but uses the same concepts still.
Note the register sets, the ALU and the Program Controller (that includes the Program Counter, Instruction Register etc.).
Most of the extra complexity here is to do with interrupts (not yet covered) or simply accessing many more types of memories.

## Slide 30: Optional: Asynchronous Machines
Used some slides from Prof.Marek Perkowski (PSU, ECE573-2009)

## Slide 31: Feedback Model for Asynchronous Sequential Networks

## Slide 32: Asynchronous FSM
Fundamental Mode Assumption
  Only one input can change at a time
    Analysis too complicated if multiple inputs are allowed to change simultaneously
  Circuit must be allowed to settle to its final value before an input is allowed to change
    Behavior is unpredictable (nondeterministic) if circuit not allowed to settle

## Slide 33: Asynch. Design Difficulties
Delay in Feedback Path
  Not reproducible from implementation to implementation
  Variable
    may be temperature or electrical parameter dependent within the same device
  Analog
    not known exactly

## Slide 34: Stable State
PS = present state
NS = next state
PS = NS = Stability
  Machine may pass through none or more intermediate states on the way to a stable state
  Desired behavior since only time delay separates PS from NS
Oscillation
  Machine never stabilizes in a single state

## Slide 35: Races
A Race Occurs in a Transition From One State to the Next When More Than One Next State Variables Changes in Response to a Change in an Input
Slight Environment Differences Can Cause Different State Transitions to Occur
  Supply voltage
  Temperature, etc.

## Slide 36: Races
01
10
11
00
PS
desired NS
if Y1 changes first
if Y2 changes first

## Slide 37: Types of Races
Non-Critical
  Machine stabilizes in desired state, but may transition through other states on the way
Critical
  Machine does not stabilize in the desired state

## Slide 38: Races
01
10
11
00
PS
desired NS
non- critical race
if Y1 changes first
if Y2 changes first
critical race
00

## Slide 39: Types of Races
Asynchronous State machines have similarities to multi-threaded software as different elements are not coherently synchronized to a single time source.
We will revisit the concept of races and stability in the context of embedded software starting in Week 5

## Slide 40: Asynchronous FSM Benefits
Fastest FSM
Economical
  No need for clock generator
Output Changes When Signals Change, Not When Clock Occurs
Data Can Be Passed Between Two Circuits Which Are Not Synchronized
In some technologies, like quantum, clock is just not possible to exist, no clocks in live organisms.

## Slide 41: Asynchronous FSM example
next
state
present
state
y1
y2
input

## Slide 42: Next State Variable
You should analyze this machine at home

## Slide 43: Asynchronous State Tables
States are either Stable or Unstable.
Stable states encircled with symbol.
Present state | Next state, output | 
 | x=0 | x=1
Q0 | Q0,0 | Q1,0
Q1 | Q2,0 | Q1,0
Q2 | Q2,0 | Q3,1
Q3 | Q0, 0 | Q3,1
Oscillations occur if all states are unstable for an input value.
Total State is a pair (x, Qi)