## Slide 1: Embedded Systems Architecture
ENGN{4,6}521
Embedded Systems

## Slide 2: Embedded System Architecture
The architecture of an Embedded System is often thought to contain hardware and hardware interfaces only. Certainly this is the portion of the Embedded System that is typically given to Electronic Engineers to design.
Embedded Systems must interact closely with their environment, so the correct definition and specification of interfaces is certainly of great importance.

## Slide 3: Typical Embedded Hardware
Processor
(Microprocessor, FPGA etc)
Domain Conversion
Sensors
UI
Actuators
Users
The World
The Machine
Environment
Power
Memories
Peripherals
Comms

## Slide 4: Embedded System Architecture
Embedded Systems typically have stricter constraints on power consumption, space, performance any many other attributes that can’t be described by the hardware alone.
The software stack forms an integral part of the overall systems architecture and must certainly be considered when designing the system.

## Slide 5: Typical Embedded Software
Processor
Microprocessor, FPGA etc.
Operating Environment
Operating System, Runtime Libraries
Application Libraries
e.g. Graphics, Communications
Application

## Slide 6: Typical Embedded System?
Processor
Microprocessor, FPGA etc.
Operating Environment
Operating System, Runtime Libraries
Application Libraries
e.g. Graphics, Communications
Application
Processor
(Microprocessor, FPGA etc)
Domain Conversion
Sensors
UI
Actuators
Users
The World
The Machine
Environment
Power
Memories
Peripherals
Comms
So is this all?

## Slide 7: Embedded System Architecture
The tight constraints surrounding Embedded Systems don’t stop at physical parameters.
The successful design of an Embedded System has to note the fact that such systems are commodities, but also that they are rarely sold as a final product.
An Embedded System architecture has to recognize the interfaces between the system and the business processes around it, not just the physical processes.
These business processes include budgets and lead times and therefore come back and affect the choice of development system as well.

## Slide 8: Typical Embedded System
Processor
Microprocessor, FPGA etc.
Operating Environment
Operating System, Runtime Libraries
Application Libraries
e.g. Graphics, Communications
Application
Processor
(Microprocessor, FPGA etc)
Domain Conversion
Sensors
UI
Actuators
Users
The World
The Machine
Environment
Power
Memories
Peripherals
Comms
Market Strategy
Reliability Specification
Development Strategy
Testing Strategy
Development Environment
Tool chain
Test Bench

## Slide 9: Typical Embedded System
Processor
Microprocessor, FPGA etc.
Operating Environment
Operating System, Runtime Libraries
Application Libraries
e.g. Graphics, Communications
Application
Processor
(Microprocessor, FPGA etc)
Domain Conversion
Sensors
UI
Actuators
Users
The World
The Machine
Environment
Power
Memories
Peripherals
Comms
Market Strategy
Reliability Specification
Development Strategy
Testing Strategy
Development Environment
Tool chain
Test Bench
Week 4
Week 5-7
Week 8
Week 9
Week 10
Week 11-12

## Slide 10: Embedded Systems as Systems
Embedded Systems are designed like all systems.
Identify Functions
Identify Interfaces
Create a Functional Architecture
Assign functions to interacting elements
Repeat the above for each element until you get to a point where each remaining element is realizable

## Slide 11: Embedded Systems as Systems
Functional Specification
Most of you will have come across the notion of specifying a system in terms of its functions during the Systems Project, System Design or otherwise in the course of your degree. It isn’t unique to Embedded Systems and is outside the scope of this course.

## Slide 12: System Interfaces
The interfaces in Embedded Systems are certainly within the scope of this course
Don’t re-invent the wheel
Know your standards
Hardware Layer
System Software Layer
Application Software Layer
Market Specific
Standards
MHP ATSC
DTV
HAVi
FDA …
General Purpose
Standards
PJava
J2ME
SSL128
…
Ethernet
TCP/IP
HTTP
…
Market-Specific Standards
  Consumer Electronics, Medical, Industrial Automation & Control, Networking & Communications, Automotive, Aerospace & Defence, Office Automation, …
General Standards
  Networking, Programming Language, Security, Quality Assurance, …
Notes: Make note that standards mentioned aren’t entirely physical entities. “Process Interfaces” like those for QA etc. count!

## Slide 13: System Interfaces
Example: Digital Television Receiver.
Standard Type | Standard
Market-Specific | Digital Video Broadcasting (DVB)
 | Java TV
 | Home audio/video interoperability (HAVi)
 | Digital Audio Video Council (DAVIC)
 | High Definition Multimedia Interface (HDMI)
 | Infrared Data Association (IrDA)
 | .. and many more
General Purpose | Hypertext Transfer Protocol (HTTP)
 | Post Office Protocol (POP3)
 | Internet Message Access Protocol (IMAP)
 | Simple Mail Transport Protocol (SMTP)
 | Java
 | Networking (TCP/UDP/IP/Ethernet/802.11)
 | POSIX
Notes: Make note that standards mentioned aren’t entirely physical entities. “Process Interfaces” like those for QA etc. count!

## Slide 14: System Interfaces
Example: Digital Television Receiver.
Systems interfaces includes things you would expect, the box has to be able to receive the digital video signal, a remote control signal and output some standard format for display on a Television (DVB, HDMI, IrDA).
The device might have functions outside its core role, such as a web interface (HTTP) or email notifications (SMTP) which in turn build on top of other standards (Ethernet/TCP/UDP/IP/802.11)
The systems interfaces also have to cover interfaces to the software as well. The ability for your Embedded System to run the target software package is just as important as any other aspect of interfacing.

## Slide 15: System Interfaces
Example: Digital Television Receiver.
Clearly most interfaces in a typical Embedded
System interfaces can be implemented against a known standard. This usually speeds up development and improves reliability as reference implementations and test benches are often parts of the standard themselves and not something that has to be implemented from scratch.
If there isn’t an applicable standard, there are often at least standard conventions. Graphical User Interfaces are an example – the notion of icons and windows as interaction metaphors has proven to scale from the Apple computers of old to the latest touchscreen enabled devices.

## Slide 16: System Interfaces
When not to standardize: When the boss tells you not to! The most typical case for not adhering to some standard protocol is that the market forces are such that interfaces must remain proprietary.
The use of proprietary standards is decreasing as companies realize that interoperability is generally desirable after all, but also that if you close an interface there are plenty of people out there interested in opening it back up. The Microsoft SMB file sharing protocol is one such example, where Andrew Tridgell (now at the ANU) reverse engineered the protocol from scratch, was sued by Microsoft but prevailed in the courts. Simply, it’s often not worth the extra time required to lock down an interface.

## Slide 17: Network Interfaces
Network 2: Client/Server Architecture
Network 1: Peer-to-Peer Architecture
Client A
Client B
Server
Client C
Device A
Device B
Device C
Transmission Medium
Network interfaces extend the Embedded System architecture beyond the physical system itself. The devices may be connected in a Client/Server fashion or a Peer-to-Peer manor.

## Slide 18: Network Interfaces
Hardware Layer
System Software Layer
Application Software Layer
Physical Layer
Data-Link Layer
Network Layer
Transport Layer
Session Layer
Presentation Layer
Application Layer
OSI Model
Within each device, the network stack can be defined in terms of the 7-layer OSI Model

## Slide 19: Network Interfaces
Hardware Layer
System Software Layer
Network Access Layer
Internet Layer
Transport Layer
Application Software Layer
Application Layer
TCP/IP Model
Physical Layer
Data-Link Layer
Network Layer
Transport Layer
Session Layer
Presentation Layer
Application Layer
OSI Model
Common protocols however generally combine or miss several of the OSI layers

## Slide 20: Network Interfaces
Common protocols however generally combine or miss several of the OSI layers
Hardware Layer
System Software Layer
Application Software Layer
Transport Protocol Group
Middleware Protocol Group
Application Protocol Group
Bluetooth Model
Physical Layer
Data-Link Layer
Network Layer
Transport Layer
Session Layer
Presentation Layer
Application Layer
OSI Model
TCP/IP
WAP

## Slide 21: Network Interfaces
Hardware Layer
System Software Layer
Application Software Layer
WAN
Wireless
CDMA
TDMA
EIA/TIA 232 (RS-232)
ATM (SONET,…)
Wired
LAN
Wireless
Wired
IEEE802.11 Wireless Radio
Bluetooth Radio
IEEE 802.3 Ethernet
IEEE 802.5 Token Ring
ARCnet
FDDI
…
TDMA
GPRS
GSM
CPDP
…
…
EIA/TIA 449 (RS-449)
X.21
EIA/TIA 232 (RS-232)
…
Six of the OSI layers are often implemented in software but the Physical Layer must be implemented in hardware

## Slide 22: Software Interfaces
The software stack is an important part of the system architecture. The way the hardware and software interact is at least as important as any other interface in the system.
Software systems are typically specified from the allocated functionality and hardware systems are selected to support these systems. This isn’t a one-way process, hardware restrictions will always come back and change software system specifications.
We’ll go over software interfaces in some detail, as they are a part of the architecture that would not have been covered in previous Engineering courses and is vital for motivating our next lectures on Embedded Processors, Operating Systems and Real Time constraints.

## Slide 23: Software Interfaces
Typical ways in which a software system will influence hardware choices:
Programming Language
  Precompiled, Just-in-time compiled, interpreted …
Operating System, Run-time Environment, Libraries
  Size, complexity, driver availability …
Memory Requirements
  A function of programming language, functions, implementations and more
Speed Requirements
  As above, influenced by a large number of software choices
Real-Time Requirements
  Not the same as speed requirements as we will see later

## Slide 24: Software Interfaces
The choice of programming language(s) is perhaps the most fundamental software architecture choice.
A balance must be struck between features, efficiency, reliability, time to market etc.
One of the key points that distinguishes programming languages from each other are whether they are precompiled, Just-in-Time compiled or Interpreted. These three options place restrictions on the locations in which a language may be used and what may be accomplished with code written in that language.

## Slide 25: Programming Languages
Precompiled code is typical of programming languages such as C, C++, ADA etc. Precompiled code doesn’t incur run-time overhead translating the programmer’s wishes to actions, however it offers less flexibility than other options.
Source Code
Compiler
Assembler
Source Code
Source Code
Source Code
Source Code
Object Files
Linker
Libraries
Executable

## Slide 26: Programming Languages
The compiler takes source code and generates machine language assembly mnemonics (written instructions such as MOV, ADD). The assembler takes this assembly, along with any that has been manually written and generates the binary object files. References to memory locations remain in symbolic form – the object file doesn’t yet know where in memory everything is going to end up.
The compiler and assembler are typically invoked with a single instruction, the intermediate assembly mnemonics are stored in a temporary file and removed upon successful generation of the object file.
The compiler is responsible for most optimizations and generation of platform-specific code. When choosing hardware, it must be selected to be compatible with the target compiler.

## Slide 27: Programming Languages
The Linker combines multiple object files (typically one per source file) along with external libraries, joins them all together in a single executable then goes through and resolves all symbols. Symbol resolution is the process of going through the executable, finding instructions that reference memory (load, store, function calls etc.) and inserting the correct memory location in to the instruction.
If static libraries are used, all symbols in the executable are resolved and no other item is required for that binary to be executed. This is typically the case for Embedded Systems.
Dynamic libraries (DLLs in Windows-speak, SOs in Linux) have their symbols left unresolved at Link time. The final memory locations for shared symbols are only resolved when the executable is run. This increases start up times but sharing code between executables can reduce overall size.

## Slide 28: Programming Languages
Just-in-time (JIT) compiled code has two processes, one on done before-hand and one done while the program runs. The intermediate representation is called ‘Byte Code’
Source Code
Byte Code Compiler
Source Code
Source Code
Source Code
Source Code
Byte Code
Source Code
JIT Compiler
Source Code
Byte Code
Offline
Online
Executable Instruction(s)

## Slide 29: Programming Languages
The JIT paradigm adds some overhead to the runtime process as the translation from byte code to machine instructions has to be done before the instruction can actually be executed. This sounds like it would take a lot of overhead, but modern JIT compilers might add just a few percent to the execution time.
JIT code means that optimization and generation of platform-specific codes are left to the platform itself, the same byte code can then be run on multiple machines. If your Embedded System and your development machine use different architectures, you can still run a single lot of code on both.
The platform itself is also usually in the best position to determine which optimizations to apply, so the overhead of JIT compilation may be reclaimed through smart application of code optimization.

## Slide 30: Programming Languages
The first stage of Interpreted code is the same as for JIT – source code is converted to byte code. When run, a special piece of software called a Virtual Machine reads each byte code in turn and decides what to do with it
JIT
Interpreted
Compile to Machine Instruction
Byte Code
Execute Instruction
Parse
Byte Code
Call function that performs required operation
Slow
Fast
Fast
Slow

## Slide 31: Programming Languages
Interpreted code has the same portability advantages as JIT code but because the code is run in a completely controlled and isolated fashion (inside a Virtual Machine), there is the possibility for increased security.
JIT compilers are widely recognized as the future of this kind of technology and are slowly replacing run-time interpreters. One exception is on obscure architectures as Virtual Machines are typically written entirely in C and can be compiled for anything supported by that compiler. JIT compilers have to be written, at least partially, specifically for a target architecture as it has to know which machine instructions to output.

## Slide 32: Programming Languages
Summary
Precompiled languages: C, C++, ADA etc. Typically older, more established languages but still very commonly used in Embedded Systems. Much low-level code such as the Linux Kernel are written in precompiled languages as there isn’t necessarily any platform upon which the JIT compiler or Virtual Machine can run.
JIT languages: Java, .NET, Dalvik since Android 2.2, Python, Javascript in some browsers. Most modern languages were either designed to be interpreted but have subsequently had JIT compilers written, or were designed for JIT execution from the start.
Interpreted languages: Typically older versions of the JIT languages above.

## Slide 33: Speed Requirements
Internal Stimulus Sources
(other internal system elements)
External Stimulus Sources
(user, data over network, etc.)
Performance Stimuli
(periodic events, one-time events, etc.)
Embedded System
Operating System
- Process events concurrently reducing response times
-Scheduler manages requests and arbitration of resources to events
-….
System Response
(events processed faster, on average, than they arrive)
System Speed Measures
(throughput, data loss, etc.)
Speed in an Embedded System can mean a number of things. In this course, speed will be used primarily as a reference to throughput. That is, “Instructions per second”, “event responses per second” etc.
A framework for sketching speed requirements is shown below

## Slide 34: Speed Requirements
Internal Stimulus Sources
(other internal system elements)
External Stimulus Sources
(user, data over network, etc.)
Performance Stimuli
(periodic events, one-time events, etc.)
Embedded System
Operating System
- Process events concurrently reducing response times
-Scheduler manages requests and arbitration of resources to events
-….
System Response Measures
(throughput, data loss, etc.)
Tactic : Resource Management
Requests
Arbitration
…
The most common architectural change to improve speed is to change the management of resources. These might be processor cycles, buffer memory, access to hardware accelerators and so on.
System Response
(events processed faster, on average, than they arrive)

## Slide 35: Responsiveness Requirements
Internal Stimulus Sources
(other internal system elements)
External Stimulus Sources
(user, data over network, etc.)
Performance Stimuli
(periodic events, one-time events, etc.)
Embedded System
Operating System
- Process events concurrently reducing response times
-Scheduler manages requests and arbitration of resources to events
-….
System Response
(events processed in timely manner, etc)
System Speed Measures
(data loss, latency, response time etc.)
Responsiveness is related to Real Time concepts as will be presented in a few lectures time. Low latency response, or rather bounded latency response, is a key aspect of all Embedded Systems
Responsiveness requirements can be couched in the same terms as speed but with slightly different metrics

## Slide 36: Responsiveness Requirements
Internal Stimulus Sources
(other internal system elements)
External Stimulus Sources
(user, data over network, etc.)
Performance Stimuli
(periodic events, one-time events, etc.)
Embedded System
Operating System
- Process events concurrently reducing response times
-Scheduler manages requests and arbitration of resources to events
-….
System Speed Measures
(data loss, latency, response time etc.)
Tactic : Resource Management
Requests
Arbitration
…
Responsiveness is improved by similar means to speed, but with different goals. Rather than increasing the number of available CPU cycles, one might increase the number of CPU Cycles reserved for the particular task
System Response
(events processed in timely manner, etc)

## Slide 37: Memory Requirements
Memory is typically one of the last requirements specified. Prototype Embedded Systems may have several times as much memory as will be required in the field to facilitate the orderly development and debugging of code.
Code with debugging information left in may be 2-3x as big as ‘Release’ code.
Memory exists in a hierarchy with larger memory sources typically slower to access.

## Slide 38: Memory Requirements
Most modern CPUs keep recently-accessed data cached in a small amount of memory tightly coupled to the CPU itself. Code rarely controls the cache itself, but can be optimized for good cache performance.
L1 Cache is typically accessed in 1-2 CPU cycles while lower level caches are proportionally slower.
In multi-core chips, the lower levels of cache may be shared between cores. This increases complexity somewhat as the cache has to remain ‘coherent’ across all cores; that is, because cache data is a copy of RAM data, it exists in at least two places at one and every core must ensure it accesses the most recent copy.
L1 CPU Cache
L2 CPU Cache
L3…
RAM
Flash
Hard Drive
Network/Cloud

## Slide 39: Memory Requirements
RAM is what we typically think of when we think of memory. In an Embedded System, some base amount is required for program variables and the rest may be used for buffering, trading off cost against throughput.
Larger RAM devices (such as Dynamic RAM) require code to execute in order to be initialized. This causes a “chicken and egg” problem; code needs RAM to execute, but the RAM needs some code to have executed. If a device is designed to use Dynamic RAM, it will typically also include a small amount of Static RAM internal to the device for the sole purpose of supporting this initial execution.
L1 CPU Cache
L2 CPU Cache
L3…
RAM
Flash
Hard Drive
Network/Cloud

## Slide 40: Memory Requirements
Flash memory is slowly replacing hard drives as the standard for local, non-volatile memory.
It is typically a few orders of magnitude slower than RAM and several orders of magnitude slower than a CPU cache.
Flash can only be written a finite number of times before it wears out, so much of the technology behind dealing with this type of memory goes in to avoiding, detecting and/or correcting errors.
Premium flash devices include Error Correcting Codes, ECC, which are special portions of memory that contain enough information to not just detect, but even fix 1, 2 or several-bit errors.
L1 CPU Cache
L2 CPU Cache
L3…
RAM
Flash
Hard Drive
Network/Cloud

## Slide 41: Memory Requirements
Aside
Modern flash memory cards such as SD cards may cheat with their wear leveling algorithms.
The FAT filesystem that is typically used on such cards writes data across the card in something approaching a round-robin fashion – in essence it does its own wear leveling. The exception to this is the File Allocation Table block which is written every time any other piece of the card is written. Given that the FAT gets written many more times than any other piece, the memory may choose to only wear level the section of the card where it thinks the FAT will sit.
This means that using a filesystem other than FAT on an SD card may reduce its lifespan 10s or 100s of times!
L1 CPU Cache
L2 CPU Cache
L3…
RAM
Flash
Hard Drive
Network/Cloud

## Slide 42: Memory Requirements
Hard Drives, or magnetic storage generally, have been around almost as long as computers themselves.
They are still the de-facto standard for high volume, non-volatile storage.
They are not often used in Embedded Systems as they are relatively power-hungry and fragile, at least when they are spinning. They also have non-deterministic response time as the magnetic heads need to physically move over the surface of the disk with each new request.
L1 CPU Cache
L2 CPU Cache
L3…
RAM
Flash
Hard Drive
Network/Cloud

## Slide 43: Memory Requirements
Network storage is becoming more fashionable as markets become less about the Embedded Device itself and more about the service it can offer. Having the service state data live externally to the system itself streamlines upgrades and can drive down system costs by centralizing much more of the system than would traditionally be the case.
Network storage has the obvious drawbacks though – the network is a weak link, both in terms of uptime and reliability, but also in terms of security.
L1 CPU Cache
L2 CPU Cache
L3…
RAM
Flash
Hard Drive
Network/Cloud