## Slide 1: Reliability and Redundancy
ENGN{4,6}521
Embedded Systems

## Slide 2: Overview
Reliability, Failure and Faults
Failure modes and fault prevention
Dynamic redundancy
Ref: Burns and Wellings Real Time Systems and Programming Languages

## Slide 3: Reliability, Failure and Faults
Sources of Faults
Inadequate Specification
Design Errors
Processor Failure
Interference on communications channels, interface faults

## Slide 4: Reliability, Failure and Faults
Sources of Faults
Inadequate Specification Not covered
Design Errors
Processor Failure Not covered
Interference on communications channels, interface faults Not covered

## Slide 5: Reliability, Failure and Faults
Sources of Faults
Inadequate Specification Not covered
Design Errors
Processor Failure Not covered
Interference on communications channels, interface faults Not covered

## Slide 6: Reliability, Failure and Faults
A system’s reliability is a measure of how well it conforms to some specification of its behaviour. A deviation from specification is called a failure.
Failures result from unexpected internal behaviour that manifests itself in the system’s external behaviour.
If a system has a problem which doesn’t manifest itself on an external interface, it cannot be called a failure.

## Slide 7: Reliability, Failure and Faults
The internal problems that result in failure are called errors and their mechanical or algorithmic cause is termed the fault.
Systems are composed of components which are themselves systems, hence
 Failure  Fault  Error  Failure  Fault 

## Slide 8: Failure Modes and Fault Prevention
Faults can be classified in the time domain
Transient Faults
e.g. communications interference
Intermittent Faults
Transient faults that occur repeatedly e.g. overheating
Persistent Faults
Stay in the system until they’re rectified by external means

## Slide 9: Failure Modes and Fault Prevention
The failures caused by the faults can also be classified
Time Domain Failures
Result or action happens at the wrong time
Value Domain Failures
Result or action isn’t correct or is inappropriate for the situation
Fail Uncontrolled
Arbitrary performance of the system as a whole
Fail Never
Ideal case!

## Slide 10: Failure Modes and Fault Prevention
Achieving Reliability
The core of a reliable system is to produce well-defined failure modes.
Fault Tolerance seeks to build systems that can provide correct function even in the face of system faults
Fault Prevention attempts to eliminate any possible sources of fault before the system becomes operational

## Slide 11: Failure Modes and Fault Prevention
Fault prevention has two stages, Fault Avoidance and Fault Removal. The successful completion of these stages depends on a thorough understanding of the system itself.
Understanding constraints on materials
Knowing boundary constraints on input and output systems
Constraints of the processor system and software
Dynamic application specifications (requested real-time behaviour)
Understanding all the critical Real Time constraints on the system!

## Slide 12: Failure Modes and Fault Prevention
Fault avoidance seeks to prevent faults entering the design and construction
Use high reliability components
Use thoroughly tested methods and techniques for assembly and interconnect
Packaging the hardware to physically prevent external interference, either on communication channels or otherwise
Rigorous (preferably formal) specification of requirements and compliance procedures
Use of proven design methodologies
Use of standardised software and hardware engineering environments to manage complexity

## Slide 13: Failure Modes and Fault Prevention
Fault Removal seeks to find and manage faults that make it through construction before the system becomes operational. Fault Removal covers aspects of the system design process such as
Design reviews
Testing procedures
Program verification
System testing
Hardware Inspection
Code Inspection

## Slide 14: Failure Modes and Fault Prevention
Fault Removal procedures should be followed throughout the design phase but selected portions will often be applied to production systems as well. The testing of production boards may cover every board off the line or some representative sample.
Often, high reliability systems will have special test tags built on to the board itself. The tag has particular patterns of copper, solder, componentry etc. which are designed to ‘stress test’ the production procedure. The tags are snapped off the boards and filed for future reference if that board develops a fault.

## Slide 15: Failure Modes and Fault Prevention
System testing can never be exhaustive and remove all potential faults. Testing can only show the presence of faults, not their absence.
It’s often hard to test under realistic conditions, much of the effort in high reliability designs may be expended in providing high fidelity test and simulation environments.

## Slide 16: Failure Modes and Fault Prevention
Recall: A system’s reliability is a measure of how well it conforms to some specification of its behaviour, a failure is a deviation from this specification.
This is important as failures are defined with respect to the specification, not with respect to actual correct behaviour! The corollary is that errors that have been introduced in the specification may not be detected until the system becomes operational.
No amount of fault avoidance and removal can guarantee operation that has not been correctly specified.

## Slide 17: Failure Modes and Fault Prevention
The system can fail despite this, a high reliability system must not allow the failure to be uncontrolled. This leads to the concept of fault tolerant systems.
This is particularly important for
Systems that are (temporarily) inaccessible
Unmanned vehicles that operate autonomously by default
Systems in remote and/or dangerous environments

## Slide 18: Failure Modes and Fault Prevention
Full fault tolerance states that the system can continue (reasonably) correct operation in the face of all ‘foreseeable’ fault conditions.
The presence of the fault condition may, however, change some system parameters such as operational lifetime.

## Slide 19: Failure Modes and Fault Prevention
Graceful degradation, also known as ‘fail-soft’, allows for the system to continue operation in the face of all ‘foreseeable’ fault conditions, accepting a reduction in functionality or performance.

## Slide 20: Failure Modes and Fault Prevention
Fail safe is the term for a failure mode in which the system remains controlled and ‘safe’ during and after a failure, as it shuts itself down.
This can also be viewed as graceful degradation to zero functionality.

## Slide 21: Failure Modes and Fault Prevention
The level of fault tolerance required will depend on the application and must be specified during the system design.
Most high reliability systems will request full fault tolerance however most settle for graceful degradation towards functionality that is not significantly reduced.

## Slide 22: Failure Modes and Fault Prevention
The method for actually implementing different levels of fault tolerance can vary. The most common method is by some means of hardware redundancy.
These extra resources may be used for
The early detection of faults that may cause failure
For the handling of exceptional situations and error recovery
As functional replacements for complete (sub)systems to facilitate hot swap procedures to remove faulty (sub)systems from operation.

## Slide 23: Failure Modes and Fault Prevention
Common fault detection and recovery hardware includes
Watchdog timers to detect when a hardware device hasn’t “checked in” for some amount of time, assume it has failed and restart it
Limit switches to detect when an actuator is being commanded to move past its maximum physical extent and shut down that actuator
Additional physical sensors to provide a “sanity check” for each other
Transient Recording Systems (emergency system dump) to at least provide a set of post-failure data to assist in analysis
Overload backup systems
etc.

## Slide 24: Failure Modes and Fault Prevention
The unit of failure is often full subsystems, with fault tolerance then acting to isolate one failed system from interfering with the overall system function.
Triple-Modular Redundancy (TMR) or N-Module Redundancy (NMR) provides multiple copies of critical subsystems which are either
Statically combined by a masking/voting/comparing system
Dynamically switched in or out depending on their operation (assumes a failure can be unequivocally detected!)

## Slide 25: Failure Modes and Fault Prevention
TMR or NMR are only useful if only one (or a small subset) of the systems fail at once. This then requires that
The source of the fault is localised to one instance of the module
The modules differ in their internal implementation sufficiently that the same fault in two modules lead to different failures or, for preference, at least once instance of no failure at all.

## Slide 26: Failure Modes and Fault Prevention
For some high risk systems, this approach is applied in the form of redundant subsystems with
The same specification
Different computer systems (CPUs, busses, memory systems, drives etc.)
Different Operating Systems
Different software development languages and environments
Even restricting the communication between different development teams

## Slide 27: Failure Modes and Fault Prevention
TMR Example: Boeing 777
Contains three identical primary flight computers, each consisting of:
Three processors: AMD 29050, Motorola 68040, Intel 80486 called ‘Lanes’. Two level redundancy!
Independent power sources and inertia measurements
Code built by three different ADA compilers
The same ADA software source code (called ‘the specification’), but with different ‘monitor’ functions written to supervise correct operation.
Targeted failure probability < 10-10 /h (e.g. UK Seizewell B Nuclear Reactor (emerg.): 10-3/h)
No single fault onboard a 777 should occur without failure identification
No single fault onboard a 777 should result in the failure of more than one flight computer

## Slide 28: Failure Modes and Fault Prevention
TMR Example: Ariane 5
The Ariane 5 rocket is a heavy-lifting platform designed to move satellites in to low-earth or geostationary orbit. In 1996, after 39 seconds of flight, the maiden launch of this platform ended in a self-destruct of the system at a cost of over $300 Million.
The Ariane 5 shared its inertial reference system with the proven Ariane 4
Ariane 5 followed a different launch trajectory to Ariane 4, but this trajectory had not been programmed in to the system simulators
Shortly after launch, the inertial reference system crashed as a result of an input velocity that was too high – it was within the Ariane 5 flight envelope, but wasn’t physically achievable on the Ariane 4 for which it had been developed
This specification mistake was common across all three redundant systems, each failed in turn, the rocket become unstable, was ripped apart due to aerodynamic forces before exploding

## Slide 29: Failure Modes and Fault Prevention
Redundancy itself isn’t a complete solution!

## Slide 30: Failure Modes and Fault Prevention
The Six Language Project
Joint project between UCLA and the Honeywell Commercial Flight Systems Division (1992) to determine which programming language provided the most reliable system outcomes.

## Slide 31: Failure Modes and Fault Prevention
The Six Language Project
The specifications (about a flight controller) were original system specification documents provided by Honeywell enhanced by additional cross-check points and included some forced diversity elements. Development teams were isolated and communication strictly controlled, defined and controlled by a central team. Specified tests were performed by the coordinating team before a version was accepted for integration. The N-Version paradigm was applied to all stages of the development cycle

## Slide 32: Failure Modes and Fault Prevention
The Six Language Project
Language | Source (l.o.c) | Test Runs | Errors | Failure Rate
Ada | 2256 | 5127400 | 0 | 0
‘C’ | 1531 | 5127400 | 568 | 1.108 x 10-4
Modula-2 | 1562 | 5127400 | 0 | 0
Pascal | 2331 | 5127400 | 0 | 0
Prolog | 2228 | 5127400 | 680 | 1.326 x 10-4
T (like LISP) | 1568 | 5127400 | 680 | 1.326 x 10-4
Average | 1913 | 5127400 | 321 | 0.624 x 10-4

## Slide 33: Failure Modes and Fault Prevention
The Six Language Project
Failure Category | Average Single Version Failure | Average Three-Version Failure | Average Five-Version Failure
No Errors | 0.99993733 | 0.9998409 | 0.9997807
Single Error | 6.27 x 10-5 | 13.05 x 10-5 | 19.15 x 10-5
Two Distinct Errors |  | 0.20 x 10-5 | 0.23 x 10-5
Two Coincident Errors |  | 2.65 x 10-5 | 2.21 x 10-5
Three Errors |  |  | 0.34 x 10-5

## Slide 34: Failure Modes and Fault Prevention
The Six Language Project
The resulting three- and five-version systems displayed lower failure rates than the ‘gold master’ reference implementation from Honeywell. Coincident failures involving more than two versions were never observed, a total of 93 faults were detected

## Slide 35: Failure Modes and Fault Prevention
TMR or NMR imply that multiple independent modules can have their results usefully compared. The truth of this statement depends somewhat on the actual form of the result.
Integer arithmetic has exactly defined results that can be compared between units in a straight-forward manner. How about other types of result?

## Slide 36: Failure Modes and Fault Prevention
Real valued results (floating point) will usually be different by some small amount, comparisons must include some concept of a tolerance rather than a blunt comparison.
If the process isn’t fully continuous (thresholds, bifurcations, quantizations) then comparisons need to re-model the whole process in order to evaluate similarities. In this process, you loose the system’s independence and therefore the value of TMR/NMR.

## Slide 37: Failure Modes and Fault Prevention
Many algorithms will have multiple results, each of which may be correct.
In order to evaluate similarities between results, the process has to be re-modeled in the same way as floating point results with the same result – independence between systems is lost and TMR/NMR is invalidated.

## Slide 38: Failure Modes and Fault Prevention
Some issues with NMR:
Specification
N-Version modules are built to the same specification so won’t help if that specification is incorrect
Diversity Assumption
Diversity can be enforced in some areas, while coincident errors are observed in others. Rigorous identification of adequate domains for N-version programming is a current source of research
Project Costs
The development costs will increase by N times, plus the cost of coordination.

## Slide 39: Dynamic Redundancy
Dynamic Redundancy is the process of identifying fault conditions during run-time and taking controlled action to rectify the fault before a system failure occurs. It consists of four phases:
Error Detection
Damage Confinement and assessment
Error Recovery
Fault Treatment

## Slide 40: Dynamic Redundancy
Error Detection is the first and most critical step of dynamic redundancy. In order to act correctly to rectify a fault before it causes a failure, the nature of the error must be understood.
Error states might be reported by the environment
Hardware: CPU, controllers, communications systems
Run-time Environment

## Slide 41: Dynamic Redundancy
Error states may also stem from the application process itself
Replication: Employ N-Version programming to detect error states
Timing: Watchdog Timers and overrun detectors
Reversal: Apply inverse function and compare, i.e. a ?= f-1(f(a))
Coding: Apply error check functions such as CRCs
Reasonableness: Apply coded ‘sanity checks’ or ‘assertions’ to results
Structural: Check structural integrity of data structures, e.g. File Systems, Lists, Databases etc.
Continuity: Assume a maximum allowable delta between successive result values

## Slide 42: Dynamic Redundancy
Confinement and Diagnosis is required once an error has been identified. The confinement condition is required to prevent the error propagating affecting external systems
‘Firewall’
Atomic Action
Modular Decomposition

## Slide 43: Dynamic Redundancy
Assessment of the error is required by analyzing the location of the error and the possible paths of propagation both towards the error state and from it. The root cause of the error may not be able to be directly measured so the reverse paths from the error location must be analyzed in order to try and determine where the root fault might lie.
The forward paths are analyzed as well in order to determine what effects the error may have had before the containment could be enacted.

## Slide 44: Dynamic Redundancy
The next step is error recovery, Forwards or Backwards:
Backwards Error Recovery
Set checkpoints and save the state of the system with each passing checkpoint.
If an error is detected, fall the entire system back to the last known good checkpoint.
Applicable even if the root error cannot be discovered.
Not applicable if any portion of the system is non-reversible, resettable or controllable (such as if a bad value gets sent across a communications channel before the system is checkpointed)

## Slide 45: Dynamic Redundancy
Forwards Error Recovery
The error is detected and the result fixed before moving on. Usually the preferred method for embedded systems. The implementation of forward error recovery is highly application specific.
In a real-time system, there may not be time for a new result to be generated; a value error becomes a timing error.

## Slide 46: Dynamic Redundancy
Once the error has been identified, contained, analyzed and recovered, the risk of failure has passed for that error.
The fault that generated that error may remain. The final stage of Dynamic Redundancy is to attempt to treat the fault that caused the initial error.
Hardware faults are usually easier to deal with than software faults. Redundant hardware modules may be switched in to place, sensors may be marked as faulty and not trusted etc.

## Slide 47: Dynamic Redundancy
Granularity in Dynamic Redundancy is usually better than normal N-Module Redundancy, however the number of redundant modules available is still limited.
Many Dynamic Redundancy systems will assume transient fault conditions and retry the same hardware at a later time, perhaps reporting a module as untrustworthy if it suffers multiple faults over some period of time.