## Slide 1: Embedded Processors
ENGN{4,6}521
Embedded Systems
The air is clean. The water is clean. Even the dirt is clean! Bowling averages are way up. Minigolf scores are way down. And we have more excellent
than any other planet we communicate with. I'm telling you, this place is great!
Ah, but don't worry: it'll all make sense. I'm a professional.

## Slide 2: Overview
CISC, RISC
Pipelining
Branch Prediction
Memory and Cache
Interrupts and Exception

## Slide 3: CISC vs RISC
Complex Instruction Set Computer vs Reduced Instruction Set Computer.
These two terms reflect two different philosophies in the design of a processor’s instruction set and, in turn, the processor architecture.
Before the 1970s, all computers were of CISC type. Memory was the supremely limited resource of the time, hardware wasn’t so much of a problem, so the focus was on packing the maximum amount of complexity in to the minimum number of instructions.
Memory is now relatively cheap and the focus has moved to performance. This favours the RISC style as simpler instructions are faster to execute

## Slide 4: CISC
CISC style is characterized by:
Complex Addressing modes
Instructions that span multiple (and variable numbers) of words
A large instruction set where specialized instructions implement particular functions
Arithmetic and Logic operations that can be performed directly on memory locations as well as registers
Memory-to-memory transfers with a single instruction
Small program sizes

## Slide 5: RISC
RISC style is characterized by:
Simple addressing modes
Single word, fixed length instructions
Small instruction set of general purpose instructions
Arithmetic and logic operations can only be performed on registers
All memory accesses though a Load/Store architecture; i.e. no instruction has both input and output in memory
Instructions designed to be implemented in (the same set of) discrete phases, lends themselves to Pipelining (to come).
Programs larger in size because more instructions are required to implement comparable functionality

## Slide 6: Hybrid Designs
Since the quantum shift from CISC to RISC styles in the 1970’s, the industry has been slowly incorporating more and more CISC-style functionality in order to reduce the number of instructions executed. This only works if the newly introduced instructions are still fast to execute. A simple example of this is single-instruction floating point operations which, by any definition, are complex operations but may be supported by dedicated FPU hardware to keep the speed up and make them fit the RISC paradigm.

## Slide 7: Hybrid Designs
Another option for hybrid designs are processors that never really moved out of the CISC era.
x86 instructions are CISC in nature, however they’re executed in a RISC core. This is done through “microinstructions” (aka microoperations, uops). The processor fetches several instructions from memory per clock cycle and dynamically translates these in to a sequence of uops. The uops are executed, potentially in parallel, then their results are re-assembled on the other side. This introduces significant extra complexity to a fully-RISC solution but maintains backwards compatibility with existing code and can actually provide the best of both worlds: Minimum program memory footprint combined with fast, pipelined execution.

## Slide 8: Pipelines
In the preceding slides, we have asserted that RISC style processors are better for pipelining, but what is pipelining and why do we want it?
Here we see the MU0 execution flow. It completes in two clock cycles but implements four operations:
Fetch
Decode
Execute
Write back
Memory operations

## Slide 9: Pipelines
This is a variation on the canonical RISC operation set:
Fetch
Decode
Execute
Memory
Write
Canonical RISC machines
take 5 clock cycles to
execute an instruction.

## Slide 10: Pipelines
Fetch
  Get the instruction out of memory
Decode
  Break down the fetched instruction and read source registers
Execute
  Fairly self-explanatory! Do the work.
Memory
  Do a memory access, either read or write depending on the operation
Write
  Write the result back to a destination register

## Slide 11: Pipelines
Example:
ADD r2, r2, r3 r2  r2 + r3
FETCH: Load instruction from memory
DECODE: Read R2, R3
EXECUTE: Perform addition
MEMORY: Do nothing
WRITE: Put ALU output in to R2

## Slide 12: Pipelines
Example:
LD r2, r3 r2  [r3]
FETCH: Load instruction from memory
DECODE: Read R3
EXECUTE: Do nothing
MEMORY: Load data from memory
WRITE: Put memory value in R2

## Slide 13: Pipelines
Many instructions don’t use all five stages, so why do they do them? Why doesn’t an add jump straight from the computation to write back? Because all modern processors PIPELINE.
F
DC
EX
ME
WB
F
DC
EX
ME
WB
F
DC
EX
ME
WB
F
DC
EX
ME
WB
F
DC
EX
ME
WB
F
DC
EX
ME
WB
1
2
3
4
5
6
1
2
3
4
5
6
7
8
9
10
Instruction
Clock Cycle

## Slide 14: Pipelines
The core observation of pipelining is this: Each instruction must take five clock cycles to complete, but you may execute more than one instruction at a time!
By breaking each instruction in to exactly the same number of pieces like this, each section of the processor can be fully utilized at every point in time.
F
DC
EX
ME
WB
F
DC
EX
ME
WB
F
DC
EX
ME
WB
F
DC
EX
ME
WB
F
DC
EX
ME
WB
F
DC
EX
ME
WB
We can answer our question from the last slide: Why keep the ME or WB stages for instructions that don’t need them? Because keeping instructions the same as each each other, they can be pipelined and the overall utilization increases significantly.

## Slide 15: Pipelines
Catch 1: Data Hazards
F
DC
EX
ME
WB
F
DC
DC
DC
DC
The Decode stage is where data from the register file is loaded in to the ALU, but what if the output of one instruction is the input for the subsequent one?
In the above example, the SUB instruction has to stall at the decode stage for three extra clock cycles before the write back of the ADD has updated the register.
EX
ME
WB
ADD R2, R3, #100
SUB R9, R2, #30

## Slide 16: Pipelines
Catch 1: Data Hazards
F
DC
EX
ME
WB
F
DC
The solution is Operand Forwarding, where the control path logic recognizes the potential for a stall and “short circuits” the result from the output of the EX stage back to its input ready for the sub, without waiting for the whole write back/decode read cycle.
This is a hardware solution, but if the hardware budget it tight, there’s a software solution: Get the compiler to re-order instructions and make sure the dependent instructions are never in the pipeline together. You don’t get the result faster, but at least you don’t waste the intermediate cycles.
EX
ME
WB
ADD R2, R3, #100
SUB R9, R2, #30
R2

## Slide 17: Pipelines
Catch 2: Memory Delays
Access to cache memory can typically be achieved in a single clock cycle. If the memory access has to go out to main memory, the pipeline may have to stall for 10s of clock cycles.
We will talk about this more when we talk about caches later in the lecture.
F
DC
EX
ME
WB
F
DC
EX
ME
WB
LDI R2, R3
SUB R9, R2, #30
ME
ME
ME
EX
EX
EX

## Slide 18: Pipelines
Catch 3: Branching
F
DC
EX
ME
WB
F
DC
EX
ME
WB
F
DC
EX
ME
WB
F
DC
EX
ME
WB
F
DC
EX
ME
WB
F
DC
EX
ME
WB
Branch Instruction
Wasted Execution
First Instruction of the new branch
If one of the instructions is a branch instruction, it will render any instructions that have already been fetched and/or partially executed irrelevant. The penalty of this depends on how late in the pipeline the CPU can determine whether or not the branch is taken. In the example above, the branch condition is tested at Execute time so the decoded instruction after it, and the fetched instruction after that, have to be removed from the pipeline.

## Slide 19: Pipelines
Catch 3: Branching
F
DC
EX
ME
WB
F
DC
EX
ME
WB
F
DC
EX
ME
WB
F
DC
EX
ME
WB
F
DC
EX
ME
WB
F
DC
EX
ME
WB
Branch Instruction
Wasted Execution
First Instruction of the new branch
Three common solutions:
Branch Delay Slot. The one or two instructions immediately following a branch are always executed. If there is useful work that can be done that doesn’t affect the outcome of the branch, it can be inserted in to this slot. If there isn’t any work, the compiler must insert NOP instructions.
The second solution (well, attempt at mitigation), is Branch Prediction. BP is implemented on almost all modern medium and large processors and the effectiveness of the BP algorithm is often a key determinant of overall performance.
Lastly, most compilers will try and work out which branch is going to be taken most often and arrange the code such that this is the fast path through the pipeline.

## Slide 20: Pipelines
The five-stage model for instruction execution, or something close, is often found implemented in RISC processors however it isn’t the only type of pipeline.
An N-stage pipeline can theoretically improve throughput N-times, so deeper pipelines should have better performance. In practice, long pipelines with many instructions executing simultaneously introduce more possibility of data interdependence and higher likelihood of stalls. Moreover, the branch penalty increases the further in to the pipeline the branch outcome is decided.
Despite this, some later Pentium 4 processors had pipelines 31 stages deep. In highly constrained devices, such as network packet processors, the pipelines may be several thousand stages deep.

## Slide 21: Superscalar Execution
We have previously shown that many instructions either require the ALU or memory access but not both. For example, a direct-addressed load requires no computation and an add involving only registers requires no memory. Processors can exploit this in order to process more than one instruction per clock cycle. This is termed Superscalar Operation. Below is shown a section of a Superscalar pipeline with two execution units, however there may be other units to cover FPU operation, single-cycle multiply or other such operations.
Fetch
Dispatch
Instruction Queue
ALU
Load/Store Unit
Write back

## Slide 22: Branch Prediction
LNT
LT
NT
NT
T
T
Two Stage branch prediction.
This assumes that the current branch will have the same outcome as the last branch. This works fairly well for loops which may be mispredicted on the first pass and will be mispredicted on the last pass. If the same loop is re-entered, and assuming the loop executes more than once, its first pass will be mispredicted as well.
T – Taken
NT – Not Taken
LT – Likely Taken
LNT – Likely Not Taken

## Slide 23: Branch Prediction
SNT
LNT
NT
T
Four Stage branch prediction.
Adding a second bit of state requires two consecutive mispredictions if the predictor has previously been ‘strongly’ conditioned. This correctly handles the first pass through the nested loop case. Note that nothing fixes the last pass misprediction.
T – Taken
NT – Not Taken
LT – Likely Taken
ST – Strongly Likely Taken
LNT – Likely Not Taken
SNT – Strongly Not Taken
LT
ST
NT
T
T
NT
NT
T

## Slide 24: Branch Prediction
A more complex scheme: Dynamic Branch Prediction Branch Target Buffer.
The CPU keeps a table which contains branch prediction state against the address of the branch instruction itself. Each time an instruction is fetched, its address is compared to addresses in the BTB and the next instruction to be fetched is determined from this state.
This changes the algorithm from predicting the future based on past branch results, to predicting the future of a particular branch based on the history of that particular branch.
The table is of course a finite size, typically around 1024 entries, which is sufficient for most repetitive tasks.

## Slide 25: Memory and Cache
Recall the memory hierarchy presented in the last lecture. There are several types of memory available to modern processors where the type chosen for a particular role is usually chosen based on a three-way trade between speed, size and cost.
The fastest type of memory is the cache memory inside the processor itself. We will discuss memories lower in the hierarchy later in the course, but today we concern ourselves only with this cache.
L1 CPU Cache
L2 CPU Cache
L3…
RAM
Flash
Hard Drive
Network/Cloud

## Slide 26: Cache
Cache works on a principle called locality of reference. Analysis of computer programs shows that most of their time is spent accessing a small subset of their overall memory. This might be due to, for example, loops, small handlers for common events, a core set of functions that call each other etc. The actual mechanism that causes locality of reference isn’t important, however the effects are.
Instructions typically live in main memory, which can take several clock cycles to access. Pipelined processors require that their instructions arrive in a single clock cycle, and Superscalar processors may look to fetch several instructions per cycle.
The only way to keep modern processors fed with instructions is to have a tightly coupled, small and fast set of memory in which the instructions most likely to be executed next are found. Such memory is called the Instruction Cache. There is also a data cache that works on a similar principle, however we will focus on the Instruction Cache in examples.

## Slide 27: Cache
Locality of Reference has two parts. First, Temporal Locality suggests that an instruction that has just been used is likely to be needed again soon. Spatial Locality suggests that when fetching one instruction it makes sense to fetch many, as they are likely to be executed next.
On these principles, a cache may be built in which chunks of main memory are cached based on how recently they were accessed or how near they were to some other piece of memory that was accessed.
These chunks are called Cache Blocks or Cache Lines.
If a memory access finds its target is already in the cache, this is called a Cache Hit, if not it is a Cache Miss.

## Slide 28: Cache
The cache is, of course, smaller than main memory so some algorithm has to be used to map a main memory location to a cache line. The simplest algorithm is called Direct Mapping. In this scheme, each memory block is stored in a cache line of the same address modulo the cache size. For example, a cache of 128 blocks will store memory block 134 in cache line number 6. DM Caches are simple but there may be contention even when the cache isn’t full.
Block 0
Block 1
Block 127
Block 128
Block 129
Block 255
Block 256
Main Memory
Line 0
Line 1
Line 127
Cache

## Slide 29: Cache
An Associative Mapping is the most flexible cache arrangement in which any memory location can be stored in any cache location. If the cache isn’t full, each new memory block can just take an empty slot. If the cache is full, the cache line to evict is chosen typically using a Least Recently Used algorithm.
Block 0
Block 1
Block 127
Block 128
Block 129
Block 255
Block 256
Main Memory
Line 0
Line 1
Line 127
Cache

## Slide 30: Cache
Block 0
Block 1
Block 127
Block 128
Block 129
Block 255
Block 256
Main Memory
Line 0
Line 2
Line 126
Cache
Line 1
Line 3
Line 127
Almost all modern caches are Set Associative. These combine the best features of each of the previous methods, as each memory location “short lists” a set of cache lines based upon its address modulo the number of sets, then the entry to evict from the set is chosen by an LRU algorithm as with an Associative cache.

## Slide 31: Cache
Cache strategies discussed previously assume a read access, but what happens for a write?
If the memory is in cache, what should a write do: Write-back and Write-through? In a write-through cache, a write to a memory location in cache will write the new value to the cache line and the memory location. Write-back writes the new value to cache and marks it dirty; it is then written to main memory only when the line is evicted.
Write-through generates unnecessary writes if the memory location is written several times in sequence. Write-back generates unnecessary writes if only one location in the cache is changed, as the whole line must be written back.

## Slide 32: Direct Memory Access
Direct Memory Access (DMA) is a technique used when large amounts of data need to be moved between peripherals and memory without any intermediate processing. Instead of requiring a processor load/store cycle, the data may be moved around without processor intervention.
Processor
DMA Controller
Memory
Peripheral
DMA Access
DMA Controller
Peripheral
Peripheral DMA
Peripheral
Traditional DMA is between a peripheral and memory, however Peripheral DMA can move data directly between different peripherals

## Slide 33: Direct Memory Access
What’s the interaction between DMA and caches?
Because the memory has multiple masters (writers), information kept in cache can’t easily be the source or destination of a DMA transfer.
Typically memory reserved for DMA transfers will be marked as un-cached and will be much slower to access from the CPU.
This issue of “Cache Coherency” is valid when ever there are multiple memory masters, such as if you have a multi-core CPU. We won’t be going in to any depth here but keep this in the back of your mind: When doing multi-CPU programming, any data that is accessed by more than one CPU can’t feel the full benefit of being cached. For more information, look in to a phenomenon called “Cache Line Bouncing”.

## Slide 34: Interrupts and Exceptions
Both Interrupts and Exceptions are events that cause the normal execution of code to be stopped and a new branch taken. They are effectively instantaneously-injected jumps.
The term Interrupt refers to such a jump that’s taken as the result of external stimuli, typically a pin on the processor undergoing a transition (high to low, low to high). An Exception has the same effect except as a response to internal conditions such as Divide by Zero (FPU Exception).
Since Exceptions can be triggered from software they are often used to break a ‘normal’ flow of code. For example, a Cache Miss as described previously might actually be implemented as an exception that executes code to load the new cache entry in.

## Slide 35: Interrupts and Exceptions
The most common use of interrupts is as a mechanism for external devices to signal to the processor that they’re in a particular state (e.g. Full of Data, Empty of Data, Too Hot, Too Cold, Too Hungry). This stops the processor “wasting” CPU cycles asking the device for this information.
Main Loop
Interrupt Routine
1
2
i
i+1
m
Interrupt happens here

## Slide 36: Interrupts and Exceptions
Interrupts are a simple concept but interact with different pieces of the CPU in often-unexpected ways.
Pipelining: Interrupts act like a branch so cause waste of partially-executed instructions. If the interrupt is injected in to the pipeline in the same way as other instructions then it may also be stalled by currently-executing commands, leading to variable interrupt latency. This is often unacceptable. One solution for periodic interrupts is to put the CPU in to a known state immediately before the interrupt is expected to occur (eg Sleep) so as to flush the pipeline and give a constant interrupt latency.
Caches and Branch Prediction: If the Interrupt Handler uses memory or branches (and it almost always will) then it will leave a legacy; it will change the timing of the code it interrupted (by more than just the time it took to execute itself!).