## Slide 1: Primer, Refresher, Reference to the C Programming Language
ENGN{4,6}521
Embedded Systems

## Slide 2: C
C is the most widely used programming language in Embedded Systems. The reason for this is simple: It’s simple. It does only and exactly what you ask it to do, though this isn’t always what you think you’ve asked it to do.
There are other languages out there that are arguably more suited to ES development; particularly Ada but also niche languages such as Esterel, Pearl, Euclid…
C provides no significant runtime environment, it stands completely on its own, but most C distributions ship with a standard set of libraries.

## Slide 3: Looping Constructs
for loop
when the number of iterations is known a-priori
while loop
when the number of iterations is data- or event-driven, possibly zero
do loop
as with the while loop, but when the enclosed code must be executed at least once
for (i = 0; i < n; i++) {
<code>
}
executed once on loop entry
condition for loop exit
executed at the end of every iteration
while (!finished) {
<code>
}
condition for loop exit
do {
<code>
} while (!finished);
condition for loop exit

## Slide 4: Looping Constructs
for loop
when the number of iterations is known a-priori
while loop
when the number of iterations is data- or event-driven, possibly zero
do loop
as with the while loop, but when the enclosed code must be executed at least once
for (d = list_head;
d->next;
d = d->next ) {
<code>
}
executed once on loop entry
condition for loop exit
executed at the end of every iteration
while (true) {
<code>
}
condition for loop exit
do {
<code>
} while (0);
condition for loop exit

## Slide 5: Branching Constructs
if statement
Complex conditions and/or few options
case statement
Many ‘equals’ conditions on a single variable
if (fu) {
confrobnicate();
} else if (bar) {
crubnuckle();
} else {
fail();
}
case (var) {
0:
is_zero();
break;
1:
2:
is_one_or_two();
break;
default:
otherwise();
}

## Slide 6: Arithmetic Operators
a = b Basic Assignment
a + b Addition
a – b Subtraction
-a Unary negation (additive inverse)
a * b Multiplication
a / b Division
a % b Modulus
++a Increment before evaluation
a++ Increment after evaluation
--a Decrement before evaluation
a-- Decrement after evaluation

## Slide 7: Binary and Boolean Operators
~a Binary negation
!a Boolean negation
a & b Binary AND operation
a && b Boolean AND operation
a | b Binary OR operation
a || b Boolean OR operation
a ^ b Binary XOR operation
a == b Boolean equals (test)
a != b Boolean not-equals
a < b Less-than
a > b Greater-than
a <= b Less-than or equal to
a >= b Greater-than or equal to
a >> n Bit-wise right shift by n places
a << n Bit-wise left shift by n places

## Slide 8: Other Operators
a[n] Array element extraction
*a Pointer dereference (value-at)
&a Reference (address-of)
a.b Structure reference (member b of structure a)
a->b Structure dereference
(member b of the structure pointed to by a)
a, b ‘Comma’, sequence point.
Evaluates each expression in turn e.g. a=1, b=3
a?b:c Turnery operator.
If ‘a’ then evaluates to b, else evaluates to c
sizeof(a) Evaluates to the number of bytes allocated for a
typeof(a) Evaluates to the data type of a
offsetof(a,b) Evaluates to the offset of member b of structure a (in bytes)

## Slide 9: Data Types
{unsigned, signed} char 8-bits. If neither signed nor unsigned is specified, the signedness is implementation-dependent.
[unsigned] short 16-bits.
[unsigned] int 16-bits on most 8-bit microcontrollers, native bit width otherwise.
[unsigned] long At least 32-bits, same as int on most 32- and 64-bit platforms.
[unsigned] long long At least 64-bits.
float IEEE single-precision floating point (usually)
double IEEE double-precision floating point (usually)
long double IEEE double- or quadruple-precision floating point
1 Number 1 as an int
1L 1 as a long
1UL 1 as an unsigned long
1.0 1 as a float
(int)(1.5) The number 1.5 cast to the integer ‘1’, not rounded up as might be expected!
(int*)0x900000000 An integer address cast to a pointer

## Slide 10: Data Types
enum a { An int-like type designed to take any of three values FU, BAR,
FU, END (which the compiler will map to integer values).
BAR,
END
};
struct a { A single data structure (record) containing two elements, an
int nub; int called ‘nub’ and a pointer to a char where the pointer is
char *nozzle; called ‘nozzle’
};

## Slide 11: Pointers
int a, *b; Declare an int called ‘a’ and a variable ‘b’ that will hold the address of an integer; i.e. is a pointer to an integer
b = &a; Set it so the pointer ‘b’ contains the address of the variable ‘a’
a = 5; Set ‘a’ to 5 directly
*b = 6; Set ‘a’ to 6 indirectly, by dereferencing the pointer

## Slide 12: Register Access
volatile int *reg = (int*)0x90008000; Create a pointer ‘reg’ whose value is the address of a register in memory. Tell the compiler not to optimize accesses to this variable.
*reg = 0x80; Write the value ‘0x80’ to the register
*reg |= (1 << 4); Set the 4th bit of the register to ‘1’
*reg &= ~(1 << 7); Clear the 7th bit of the register